## Slide 1: US Army Corps of engineers los Angeles district
City of Phoenix Natural/Cultural Resource Regulatory Compliance Consultant Workshop
    Regulatory Program
    Section 404 Clean Water Act Permitting
January 30, 2025

## Slide 2: Regulatory Program Overview
Geographic Jurisdiction
General Permits
Letters of Permission
Individual Permits

## Slide 3: Regulatory Overview
Mission Statement:
To protect the Nation’s aquatic resources, while allowing reasonable development through fair, timely and balanced permit decisions.
Authorities:
Section 404 of the Clean Water Act
Section 10 of the Rivers and Harbors Act of 1899
Section 103 of the Marine Protection, Research, and Sanctuaries Act of 1972
Notes: Section 103 is used for ocean disposal, which does not occur in AZ.

## Slide 4: What is Section 404?
Section 404 of the Clean Water Act (1972, as amended)
Required for the discharge of dredged or fill material into waters of the U.S.
Common projects are construction, maintenance, and repair activities in the waters of the U.S.
IMPORTANT NOTES
Not all waters are waters of the U.S.
The State may have a different definition of waters – BOTH apply!
Notes: The term “Section 404” refers to Section 404 of the Clean Water Act, initially published in 1972. Under this authority, the Corps regulates the discharge of dredged or fill material into WOTUS.
Fill is anything that replaces an aquatic feature with dry land or that raises a resource’s bottom elevation.
Common projects include construction, maintenance, and repairs within WOTUS.
Not all waters are WOTUS – we must take jurisdiction. I will explain more in the next slides.
The State may define regulated waters differently. If that is the case, both definitions apply and the project must comply with all applicable regulations whether federal, state, tribal, or local.

## Slide 5: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: Here is a brief outline of how the Corps determines if a permit is needed and which permit/permits apply.
Every project starts with 2 questions:
Let’s start with geographic authority.

## Slide 6: Amended 2023 rule
Arizona is currently evaluating jurisdiction under the Amended 2023 Rule - Revised Definition of “Waters of the United States”; effective September 8, 2023
(may also be referred to as the “conforming rule”)
Categories of Jurisdictional Waters
(a)(1)
(i) Traditional Navigable Waters
(ii) Territorial Seas
(iii)Interstate Waters
(a)(2) Impoundments of Jurisdictional Waters
(a)(3) Tributaries
(a)(4) Adjacent Wetlands
(a)(5) Intrastate lakes and ponds
that do not fall within (a)(1) – (a)(4)

## Slide 7: Amended 2023 rule - tributaries
Tributaries include natural, man-altered, or man-made water bodies that flow directly or indirectly into (a)(1) waters or (a)(2) impoundments.
Tributaries can include rivers, streams, lakes, ponds, and impoundments.
Tributaries can also include ditches and canals.
Jurisdictional tributaries must meet the relatively permanent standard.
Relatively Permanent Standard
Relatively permanent waters include tributaries
that have flowing or standing water year-round
or continuously during certain times of year.
Relatively permanent waters do not include
tributaries with flowing or standing water for only
a short duration in direct response to precipitation.
Ephemeral streams are not considered relatively permanent.

## Slide 8: Jurisdictional Determinations
Approved Jurisdictional Determination (JD)
Binding
Definitive regarding non-jurisdictional areas
May require EPA coordination
Low priority actions for Regulatory staff
Timing: 6-9 months
Can be appealed
Preliminary JD
Non-Binding
Assume all likely areas are jurisdictional
No EPA coordination
Allows projects to move forward
Not for use on clear non-relatively permanent waters
Notes: Again, not all waters are WOTUS. The Corps uses a process called a JD to determine if an aquatic resource is subject to Section 404.
Currently operating under the 2023 Rule which became effective on March 20th. There is a stay of this Rule in several states, but it remains effective in the State of AZ.
There are 2 types of JDs, approved and preliminary.
An AJD is a binding decision that provides definitive answers whether or not an aquatic resource is jurisdictional under the current definition of WOTUS. This type often requires a SNA, which is a lengthy process used to evaluate the connection between the resource and a downstream navigable or interstate water. All AJDs must be coordinated with EPA.
A PJD is not binding because instead of determining whether a resource is jurisdictional, a PJD assumes that all aquatic resources in the project area are jurisdictional. This method would confirm the location and OHWMs of the resources. There is no SNA and no EPA coordination and has a quick turnaround.
The photos are actual submissions to show the extent of each type of request. A few pages vs a binder.

## Slide 9: Jurisdictional Determinations, cont’d
Way forward:
May be further changes to the definition of Waters of the United States; some litigation on-going
Applicants may still pursue a PJD if desired for intermittent or perennial waterways.
[Generally we will not be doing PJDs on ephemeral or non-relatively permanent waters.]

## Slide 10: Resources for jds
Need sources to support flow regime (RPW or non-RPW) and connection to downstream navigable waterway
National Hydrography Dataset (NHD Plus)
ADEQ GIS
EPA website
Google Earth
Site visit photos
Stream Duration Assessment Method
SDAMs are rapid field assessment methods that use hydrological, geomorphological, and/or biological indicators, observable in a single site visit, with or without geospatial indicators to classify streamflow duration as perennial, intermittent, or ephemeral at the stream reach scale.
Not required, but an available tool if needed.

## Slide 11: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: Back to our process questions – once we know the Corps has geographic authority, we need to know if there are regulated activities.

## Slide 12: Regulated activities
Any activity that results in ground-disturbing activities (i.e., dredging or filling) within waters of the U.S.
Fills (e.g., construction of buildings, parking lots, etc.)
Roads (culverts)
Rip-rap
Grading (moving material from one area to another within the waterway)
Stockpiles
Utility lines
Mechanized removal of vegetation

## Slide 13: Activities not regulated under section 404
Excavation – “scoop and haul”
Fences
Driving
Herbicides
Other activities regulated by Section 402 (SWPPP)
Exemptions
Maintenance of structures such as dams, dikes, and levees (return to as-built condition)
Maintenance (but not construction) of drainage ditches (see 33 CFR Part 323.4(a)(2))
Notes: Here are some activities that are not regulated.
Section 404 also defines a few activities which are exempt from permitting requirements. The most relevant are:

## Slide 14: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: If we answered both questions “yes” then a Section 404 permit is required and we have to determine what type is most appropriate.

## Slide 15: Project scope
Location information
  Vicinity map
  Coordinates
  Directions to site
  Permission to access
Clearly define project area boundary
Describe all proposed activities
  Single and complete project
Recent, good-quality aerial imagery
Notes: It is important to know the full scope of the project to best determine the type of permit to use. This information would all be part of a permit application or pre-construction notification.
Include location, project boundary, description of activities proposed in WOTUS, area of disturbance, photos, aerial imagery, etc.

## Slide 16: Nationwide permits
Corps reviews and reissues the Nationwide Permit (NWP) Program every 5 years
Current set of NWPs:
  57 valid NWPs issued in 2021
  Expire March 14, 2026
Verification letter from Corps generally valid until March 14, 2026 (with one additional year if work is started by March 14, 2026)
Includes general conditions and permit-specific conditions
Regional conditions added at District/Division level – Districts consult/work with Tribal governments and federal/state agencies
May be able to proceed with a non-notifying NWP
Notes: Every 5 years, the Nationwide Permits are reviewed and reissued, sometimes with minor modifications. The current set of 59 NWPs was issued in 2021 and will expire on March 14, 2026.
NWP verification letters issued by the Corps are generally valid until that expiration date.
Each NWP has terms and conditions associated with the authorization, including regional conditions that are worked out among the District and other agencies and Tribes before re-issuance. Additional project-specific conditions may also be added to the verification letter, as necessary.

## Slide 17: Emergency permits
Regional General Permit (RGP) 63
Minimal Effects Statutory Requirement
Necessary repair and protection measures to address emergency
Emergency = clear, sudden, unexpected, and imminent threat to life or property
  Immediate action to prevent or mitigate loss or, or damage to, life, health, property
  Potential to result in unacceptable hazard to life or a significant loss of property if corrective action requiring a permit is not taken quickly
Notes: Sallie start.

## Slide 18: Emergency Permits
RGP63 – Pre-Construction Notification Required
  Must notify Corps Regulators in advance of work in waters of the U.S.
  Corps transmits interagency resource notification prior to verification/authorization
  Authorization issued in hours to days; no “after-the-fact” use
  Unilateral decision to proceed in high threat/off hours situations requires attempt to reach Corps staff prior to work
    Transmit to Regulatory office by telephone, email, delivered written notice, or other alternative means

## Slide 19: Regional general permits
RGP 41 - Eradication and Removal of Invasive, Non-Native Plant and Algal
RGP 41 may be used to authorize activities in waters of the U.S. involving the discharge of dredged or fill material and structures or work in or affecting navigable waters associated with the eradication and removal of the invasives from waters of the U.S., including wetlands for the purposes of aquatic habitat enhancement and restoration
RGP 104 - Wildfire Mitigation Activities
RGP 104 may be used to authorize activities in waters of the United States involving the discharge of dredged or fill material and structures or work in or affecting navigable waters associated with wildfire mitigation, including wildfire protection, prevention, response, clean-up, and recovery.

## Slide 20: Section 404 letter of permission (lop)
LOPs are a type of individual permit issued through an abbreviated processing procedure which includes coordination with federal and state fish and wildlife agencies, but without publishing an individual public notice.
Activities proposed under this LOP procedure are subject to the following thresholds: a. The permanent loss of waters of the U.S. shall not exceed one (1) acre. b. The permanent loss of waters of the U.S. shall not exceed 1,000 linear feet of streambed.
Activities to be authorized include, but are not limited to: residential, commercial, industrial, recreational, agricultural, and municipal development; renewable energy; transportation, infrastructure, and utility lines; mining; flood and sea level rise protection; storm-water management and polishing; survey, research, testing and monitoring; environmental remediation, restoration, and enhancement; repair, rehabilitation, and maintenance; and hydropower, reclamation, and reuse facilities.

## Slide 21: LOP - continued
Apply using the standard application (ENG FORM 4345) or use the Regulatory Request System (RRS)
Location information
Clearly define project area boundary, including waters of the U.S.
Describe all proposed activities, including acreage and avoidance and minimization measures
Alternatives considered
Compensatory Mitigation proposal
Evaluation of impacts to T&E species, cultural resources; 401 certification/application

## Slide 22: Individual Permits
Permitting path for larger, more complex activities, that don’t fit within general permit parameters
Longer processing period; 6 to 9 months to several years depending on complexity and involvement with other agencies
Corps issues public notice to solicit input from agencies, tribes, and interested members of the public
Requires alternatives analysis and identification of a “least environmentally damaging practicable alternative” (LEDPA)

## Slide 23: Additional permitting considerations
Section 401 Clean Water Act
  Water quality certifications (WQCs) issued by AZDEQ, Tribes or EPA
  Some NWPs and RGPs have blanket WQCs
Section 7 of Endangered Species Act (ESA)
  Coordination with USFWS
Section 106 of National Historic Preservation Act (NHPA)
  Coordination with AZ State Historic Preservation Office and Tribes
Compensatory Mitigation
Section 408 – required for activities near Corps-built or designed structures
Early and continuous coordination and resource management is key!

## Slide 24: Regulatory request system
New requests for a pre-application meeting, jurisdictional determination, or permit should be submitted through the Regulatory Request System (RRS) at rrs.usace.army.mil.
System will walk through all the required information to be submitted.
You can also report a potential violation using the RRS.
You can comment on a public notice using the RRS.
Other requests will continue to be accepted in digital format through the general email address for Los Angeles District Regulatory.
After your request is received, a Regulatory Project Manager and identification number will be assigned. After assignment, submit any additional information or documentation for your request directly to the Regulatory Project Manager.

## Slide 25: Compliance and Enforcement
Necessary components for an effective regulatory program
Corps PMs have responsibility for ensuring permit conditions are being met and permitted activities are in compliance
Unauthorized activities (UAs), not related to a permitted activity, may be observed in the field or reported by other agencies or members of the public
UAs are typically initially investigated by Corps PMs.
Coordination between Corps and EPA occurs under a field-level agreement

## Slide 26: Regulatory outlook
Corps Regulatory staff coordinate closely with the City of Phoenix on any activities within city limits. “Find out First” with the City and the Corps Project Manager.
Budget cuts and hold on hiring (local to South Pacific Division/Los Angeles District only); federal hiring freeze
Several Project Managers have left Regulatory will depart within the next year.
Arizona staff have been working on projects outside our usual area (Southern California, Florida, etc.)
Maximize efficiency
    JD is not required (however coordinate with the City of Phoenix)
    Regulatory may respond with an email vs. formal letter
    Request a pre-application meeting to get baseline info

## Slide 27: Questions?
Thank you!
3636 N. Central Ave, Suite 900
Phoenix, AZ 85012-1939
Regulatory Request System: rrs.usace.army.mil
General Phone: 602-230-6949
splregulatoryaz@usace.army.mil