## Slide 1: Welcome to the Natural/Cultural Resource Regulatory Workshop
Presentations will start at 8:00am

## Slide 2: US Army Corps of engineers los Angeles district
City of Phoenix Natural/Cultural Resource Regulatory Compliance Consultant Workshop
    Regulatory Program
    Section 404 Clean Water Act Permitting
January 30, 2025

## Slide 3: Regulatory Program Overview
Geographic Jurisdiction
General Permits
Letters of Permission
Individual Permits

## Slide 4: Regulatory Overview
Mission Statement:
To protect the Nation’s aquatic resources, while allowing reasonable development through fair, timely and balanced permit decisions.
Authorities:
Section 404 of the Clean Water Act
Section 10 of the Rivers and Harbors Act of 1899
Section 103 of the Marine Protection, Research, and Sanctuaries Act of 1972
Notes: Section 103 is used for ocean disposal, which does not occur in AZ.

## Slide 5: What is Section 404?
Section 404 of the Clean Water Act (1972, as amended)
Required for the discharge of dredged or fill material into waters of the U.S.
Common projects are construction, maintenance, and repair activities in the waters of the U.S.
IMPORTANT NOTES
Not all waters are waters of the U.S.
The State may have a different definition of waters – BOTH apply!
Notes: The term “Section 404” refers to Section 404 of the Clean Water Act, initially published in 1972. Under this authority, the Corps regulates the discharge of dredged or fill material into WOTUS.
Fill is anything that replaces an aquatic feature with dry land or that raises a resource’s bottom elevation.
Common projects include construction, maintenance, and repairs within WOTUS.
Not all waters are WOTUS – we must take jurisdiction. I will explain more in the next slides.
The State may define regulated waters differently. If that is the case, both definitions apply and the project must comply with all applicable regulations whether federal, state, tribal, or local.

## Slide 6: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: Here is a brief outline of how the Corps determines if a permit is needed and which permit/permits apply.
Every project starts with 2 questions:
Let’s start with geographic authority.

## Slide 7: Amended 2023 rule
Arizona is currently evaluating jurisdiction under the Amended 2023 Rule - Revised Definition of “Waters of the United States”; effective September 8, 2023
(may also be referred to as the “conforming rule”)
Categories of Jurisdictional Waters
(a)(1)
(i) Traditional Navigable Waters
(ii) Territorial Seas
(iii)Interstate Waters
(a)(2) Impoundments of Jurisdictional Waters
(a)(3) Tributaries
(a)(4) Adjacent Wetlands
(a)(5) Intrastate lakes and ponds
that do not fall within (a)(1) – (a)(4)

## Slide 8: Amended 2023 rule - tributaries
Tributaries include natural, man-altered, or man-made water bodies that flow directly or indirectly into (a)(1) waters or (a)(2) impoundments.
Tributaries can include rivers, streams, lakes, ponds, and impoundments.
Tributaries can also include ditches and canals.
Jurisdictional tributaries must meet the relatively permanent standard.
Relatively Permanent Standard
Relatively permanent waters include tributaries
that have flowing or standing water year-round
or continuously during certain times of year.
Relatively permanent waters do not include
tributaries with flowing or standing water for only
a short duration in direct response to precipitation.
Ephemeral streams are not considered relatively permanent.

## Slide 9: Jurisdictional Determinations
Approved Jurisdictional Determination (JD)
Binding
Definitive regarding non-jurisdictional areas
May require EPA coordination
Low priority actions for Regulatory staff
Timing: 6-9 months
Can be appealed
Preliminary JD
Non-Binding
Assume all likely areas are jurisdictional
No EPA coordination
Allows projects to move forward
Not for use on clear non-relatively permanent waters
Notes: Again, not all waters are WOTUS. The Corps uses a process called a JD to determine if an aquatic resource is subject to Section 404.
Currently operating under the 2023 Rule which became effective on March 20th. There is a stay of this Rule in several states, but it remains effective in the State of AZ.
There are 2 types of JDs, approved and preliminary.
An AJD is a binding decision that provides definitive answers whether or not an aquatic resource is jurisdictional under the current definition of WOTUS. This type often requires a SNA, which is a lengthy process used to evaluate the connection between the resource and a downstream navigable or interstate water. All AJDs must be coordinated with EPA.
A PJD is not binding because instead of determining whether a resource is jurisdictional, a PJD assumes that all aquatic resources in the project area are jurisdictional. This method would confirm the location and OHWMs of the resources. There is no SNA and no EPA coordination and has a quick turnaround.
The photos are actual submissions to show the extent of each type of request. A few pages vs a binder.

## Slide 10: Jurisdictional Determinations, cont’d
Way forward:
May be further changes to the definition of Waters of the United States; some litigation on-going
Applicants may still pursue a PJD if desired for intermittent or perennial waterways.
[Generally we will not be doing PJDs on ephemeral or non-relatively permanent waters.]

## Slide 11: Resources for jds
Need sources to support flow regime (RPW or non-RPW) and connection to downstream navigable waterway
National Hydrography Dataset (NHD Plus)
ADEQ GIS
EPA website
Google Earth
Site visit photos
Stream Duration Assessment Method
SDAMs are rapid field assessment methods that use hydrological, geomorphological, and/or biological indicators, observable in a single site visit, with or without geospatial indicators to classify streamflow duration as perennial, intermittent, or ephemeral at the stream reach scale.
Not required, but an available tool if needed.

## Slide 12: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: Back to our process questions – once we know the Corps has geographic authority, we need to know if there are regulated activities.

## Slide 13: Regulated activities
Any activity that results in ground-disturbing activities (i.e., dredging or filling) within waters of the U.S.
Fills (e.g., construction of buildings, parking lots, etc.)
Roads (culverts)
Rip-rap
Grading (moving material from one area to another within the waterway)
Stockpiles
Utility lines
Mechanized removal of vegetation

## Slide 14: Activities not regulated under section 404
Excavation – “scoop and haul”
Fences
Driving
Herbicides
Other activities regulated by Section 402 (SWPPP)
Exemptions
Maintenance of structures such as dams, dikes, and levees (return to as-built condition)
Maintenance (but not construction) of drainage ditches (see 33 CFR Part 323.4(a)(2))
Notes: Here are some activities that are not regulated.
Section 404 also defines a few activities which are exempt from permitting requirements. The most relevant are:

## Slide 15: Regulatory Process
Is there geographic authority (jurisdiction)?
Are there regulated activities?
If both yes
What is the scope of the project?
What type of permit is needed?
It all starts with TWO BIG QUESTIONS:
Notes: If we answered both questions “yes” then a Section 404 permit is required and we have to determine what type is most appropriate.

## Slide 16: Project scope
Location information
  Vicinity map
  Coordinates
  Directions to site
  Permission to access
Clearly define project area boundary
Describe all proposed activities
  Single and complete project
Recent, good-quality aerial imagery
Notes: It is important to know the full scope of the project to best determine the type of permit to use. This information would all be part of a permit application or pre-construction notification.
Include location, project boundary, description of activities proposed in WOTUS, area of disturbance, photos, aerial imagery, etc.

## Slide 17: Nationwide permits
Corps reviews and reissues the Nationwide Permit (NWP) Program every 5 years
Current set of NWPs:
  57 valid NWPs issued in 2021
  Expire March 14, 2026
Verification letter from Corps generally valid until March 14, 2026 (with one additional year if work is started by March 14, 2026)
Includes general conditions and permit-specific conditions
Regional conditions added at District/Division level – Districts consult/work with Tribal governments and federal/state agencies
May be able to proceed with a non-notifying NWP
Notes: Every 5 years, the Nationwide Permits are reviewed and reissued, sometimes with minor modifications. The current set of 59 NWPs was issued in 2021 and will expire on March 14, 2026.
NWP verification letters issued by the Corps are generally valid until that expiration date.
Each NWP has terms and conditions associated with the authorization, including regional conditions that are worked out among the District and other agencies and Tribes before re-issuance. Additional project-specific conditions may also be added to the verification letter, as necessary.

## Slide 18: Emergency permits
Regional General Permit (RGP) 63
Minimal Effects Statutory Requirement
Necessary repair and protection measures to address emergency
Emergency = clear, sudden, unexpected, and imminent threat to life or property
  Immediate action to prevent or mitigate loss or, or damage to, life, health, property
  Potential to result in unacceptable hazard to life or a significant loss of property if corrective action requiring a permit is not taken quickly
Notes: Sallie start.

## Slide 19: Emergency Permits
RGP63 – Pre-Construction Notification Required
  Must notify Corps Regulators in advance of work in waters of the U.S.
  Corps transmits interagency resource notification prior to verification/authorization
  Authorization issued in hours to days; no “after-the-fact” use
  Unilateral decision to proceed in high threat/off hours situations requires attempt to reach Corps staff prior to work
    Transmit to Regulatory office by telephone, email, delivered written notice, or other alternative means

## Slide 20: Regional general permits
RGP 41 - Eradication and Removal of Invasive, Non-Native Plant and Algal
RGP 41 may be used to authorize activities in waters of the U.S. involving the discharge of dredged or fill material and structures or work in or affecting navigable waters associated with the eradication and removal of the invasives from waters of the U.S., including wetlands for the purposes of aquatic habitat enhancement and restoration
RGP 104 - Wildfire Mitigation Activities
RGP 104 may be used to authorize activities in waters of the United States involving the discharge of dredged or fill material and structures or work in or affecting navigable waters associated with wildfire mitigation, including wildfire protection, prevention, response, clean-up, and recovery.

## Slide 21: Section 404 letter of permission (lop)
LOPs are a type of individual permit issued through an abbreviated processing procedure which includes coordination with federal and state fish and wildlife agencies, but without publishing an individual public notice.
Activities proposed under this LOP procedure are subject to the following thresholds: a. The permanent loss of waters of the U.S. shall not exceed one (1) acre. b. The permanent loss of waters of the U.S. shall not exceed 1,000 linear feet of streambed.
Activities to be authorized include, but are not limited to: residential, commercial, industrial, recreational, agricultural, and municipal development; renewable energy; transportation, infrastructure, and utility lines; mining; flood and sea level rise protection; storm-water management and polishing; survey, research, testing and monitoring; environmental remediation, restoration, and enhancement; repair, rehabilitation, and maintenance; and hydropower, reclamation, and reuse facilities.

## Slide 22: LOP - continued
Apply using the standard application (ENG FORM 4345) or use the Regulatory Request System (RRS)
Location information
Clearly define project area boundary, including waters of the U.S.
Describe all proposed activities, including acreage and avoidance and minimization measures
Alternatives considered
Compensatory Mitigation proposal
Evaluation of impacts to T&E species, cultural resources; 401 certification/application

## Slide 23: Individual Permits
Permitting path for larger, more complex activities, that don’t fit within general permit parameters
Longer processing period; 6 to 9 months to several years depending on complexity and involvement with other agencies
Corps issues public notice to solicit input from agencies, tribes, and interested members of the public
Requires alternatives analysis and identification of a “least environmentally damaging practicable alternative” (LEDPA)

## Slide 24: Additional permitting considerations
Section 401 Clean Water Act
  Water quality certifications (WQCs) issued by AZDEQ, Tribes or EPA
  Some NWPs and RGPs have blanket WQCs
Section 7 of Endangered Species Act (ESA)
  Coordination with USFWS
Section 106 of National Historic Preservation Act (NHPA)
  Coordination with AZ State Historic Preservation Office and Tribes
Compensatory Mitigation
Section 408 – required for activities near Corps-built or designed structures
Early and continuous coordination and resource management is key!

## Slide 25: Regulatory request system
New requests for a pre-application meeting, jurisdictional determination, or permit should be submitted through the Regulatory Request System (RRS) at rrs.usace.army.mil.
System will walk through all the required information to be submitted.
You can also report a potential violation using the RRS.
You can comment on a public notice using the RRS.
Other requests will continue to be accepted in digital format through the general email address for Los Angeles District Regulatory.
After your request is received, a Regulatory Project Manager and identification number will be assigned. After assignment, submit any additional information or documentation for your request directly to the Regulatory Project Manager.

## Slide 26: Compliance and Enforcement
Necessary components for an effective regulatory program
Corps PMs have responsibility for ensuring permit conditions are being met and permitted activities are in compliance
Unauthorized activities (UAs), not related to a permitted activity, may be observed in the field or reported by other agencies or members of the public
UAs are typically initially investigated by Corps PMs.
Coordination between Corps and EPA occurs under a field-level agreement

## Slide 27: Regulatory outlook
Corps Regulatory staff coordinate closely with the City of Phoenix on any activities within city limits. “Find out First” with the City and the Corps Project Manager.
Budget cuts and hold on hiring (local to South Pacific Division/Los Angeles District only); federal hiring freeze
Several Project Managers have left Regulatory will depart within the next year.
Arizona staff have been working on projects outside our usual area (Southern California, Florida, etc.)
Maximize efficiency
    JD is not required (however coordinate with the City of Phoenix)
    Regulatory may respond with an email vs. formal letter
    Request a pre-application meeting to get baseline info

## Slide 28: Questions?
Thank you!
3636 N. Central Ave, Suite 900
Phoenix, AZ 85012-1939
Regulatory Request System: rrs.usace.army.mil
General Phone: 602-230-6949
splregulatoryaz@usace.army.mil

## Slide 29
Regulations for Consultants

## Slide 30: Why am I here?
The U.S. Fish and Wildlife Service’s mission of:
“Working with others to conserve, protect and enhance fish, wildlife, plants and their habitats for the continuing benefit of the American people.”​
Endangered Species Act of 1973
Notes: I’m here talking to you because of the mission, and charge, of the U.S. Fish and Wildlife Service (or Service) of “Working with others to conserve, protect, and enhance fish, wildlife, plants, and their habitats for the continuing benefit of the American People.” I am also here to provide guidance on endangered species, and the Endangered Species Act.
You all here represent the “working with others.” Together, we can work to conserve, protect, and enhance wildlife, plants and habitats through the ESA of 1973. The ESA is made up of a several sections, but importantly for our discussions are Sections 7, and 10 which all deal with projects and how to see those projects through while considering the needs of these imperiled species so that an ESA Section 9 violation, which is that take of listed species is unlawful, doesn’t occur. Section 10 projects are very intensive and not as common, so today I will only be covering Section 7.

## Slide 31: Why are you here?
  You work on projects that need permits (Clean Water Act), environmental compliance (NEPA), etc.
  You work on projects on behalf of, or in partnership with, a federal agency.
Notes: Which makes you either the action agency, or a representative of the action agency. And under section 7 of the ESA, consultation should be completed for any action that is permitted/approved or funded by a federal agency and that has an effect on listed species or their critical habitat.
Yuma Ridgway’s Rail. Photo: Claudio Contreras Koob

## Slide 32: First: Is there an effect?
Before anything, please visit IPaC: (https://ipac.ecosphere.fws.gov/)
Then:
Input your project area and project type into the system. It will likely note that T/E species are in your area.
Request an Official Species List.
Congratulations you’ve now coordinated with the USFWS!
Review the list, consider where you are, and what you’re doing when.
Notes: Before getting into the section 7 consultation process, a preliminary evaluation needs to occur regarding whether any part of your project will have an effect on listed species or their critical habitat. To determine those potential species, and critical habitat present in your project area, you can visit IPaC.
Requesting an official species list through IPaC is a certified way to show that preliminary coordination with the Service because the auto-generated letter is electronically signed by our Arizona Office and is on official letterhead. To note, the ranges for species in IPaC are broad, so just because a species comes up in your list doesn’t mean it’s there. Which is where you, as the project expert come in to review if there are important habitat features that could mean doing surveys. Key habitats to look for regarding some key Phoenix-species: - cottonwood and willow stands, -mesquite stands, -cattail/marsh habitat, -milkweed, -dense living tamarisk stands.
#4 is likely the most important part of this because only you as the project-proponent (action-agency) can make the determination of if there could be an effect. If you are working on behalf of a Federal Agency, you can make this determination for them, but either way the “action agency” is responsible for keeping a good record for this decision.
There are three different determinations you can make:
1. No effect. Meaning there is absolutely no effect to any listed species.
2. May effect, not likely to adversely affect. Meaning that there could be an effect, but any such effect is incredibly unlikely to occur, or couldn’t be measured.
3. May effect, likely to adversely affect. Meaning that effects that could occur are likely and/or could have a measurable effect on the species or its critical habitat.
Examples: You input your project area and the species list pulls up the threatened yellow-billed cuckoo.
You’re working on behalf of HUD, or with HUD funding, to remodel a housing complex in the middle of Phoenix.- Consider a no effect call. There is no habitat, and no foreseeable way a cuckoo could be affected.
You’re using Federal Highways Funding to help repair a bridge that crosses a section of waterway with cottonwoods and willows from November-January.- Consider a may affect, not likely to adversely affect. The heavy equipment could cause noise that would affect any present cuckoos, but this is outside the nesting season so measurable effects are not expected. If any habitat is removed during this project, it would be unlikely to affect any nesting attempts.
You’re using Federal Highways Funding to help repair a bridge that crosses a section of waterway with cottonwoods and willows from April-June.- Consider a may affect, likely to adversely effect. You’re now in the nesting/breeding season for cuckoos, so any noise or habitat changes could result in negative impacts to nesting attempts.
You’re using a 404 Permit issued by the U.S. Army Corps of Engineers for instream work replanting trees to improve habitat- Depending on the time of year, and what equipment is being used, this could be a may affect, likely to adversely impact even though overall the project is beneficial.
Only you/your agency can make a determination. The Service does not offer concurrences for no-effect determinations. We can offer Technical Assistance if requested.
If you make a no-effect determination, you don’t need to contact the Service. This is where we, as the Service, are operating on a basis of trust.
If you think there could be an effect, even if the project is overall beneficial to wildlife, then we need to consider the next phase!

## Slide 33: Is there a Federal Nexus?
Meaning, is there any funding, personnel, land, permits, or otherwise that is tied to a Federal agency, even if just funding?
Clean Water Act Permit
FEMA
U.S. Army Corp. of Engineers Permit
Federal Highways Administration
Housing and Urban Development (HUD)
etc.
Notes: The Federal agency involved (funding, permitting, or workers) is the responsible party (Action Agency). If there is an effect to T/E species the consultant may complete the environmental compliance (BA) on behalf of the Action Agency.
Having a Federal Nexus is the easiest way to get that authorization if you think there could be an effect.

## Slide 34: Federal Nexus: Yes
Contact the Office of Environmental Programs.
The OEP will instruct you on who/how to reach out to the Federal-Agency POC.
Let the Federal Agency POC know there might be an effect with your project.
That POC should then coordinate with the USFWS with any necessary consultation.
Notes: If there is a Federal Nexus, a Biological Assessment is submitted to the appropriate Service office, and either a concurrence consultation or a Biological Opinion are returned. There is no permit associated with a Section 7 consultation. If there is “take” of listed species the Section 7 Biological Opinion will authorize that take.

## Slide 35: Key Information to Include
Some information is more important:
Start and end dates for the project
What will be done
Where it will be done
How the project will be done
  Bulldozer for X days?
  Will an access road be needed? Is it existing or to be created?
  Etc.
Why will it be done.
What species and/or habitat you determined would be affected.
What measures will be taken to minimize effects to the species and/or habitat.
Notes: It’s possible the Federal agency POC will ask that you write the Biological Assessment. If this happens the more information you can give us at the beginning the better and easier, it’ll be. In gist, it’s the WHO, WHAT, WHEN, WHERE, WHY, and HOW.

## Slide 36: Federal Nexus: No
Contact the Office of Environmental Programs.
Notes: If there is no federal nexus no section 7 consultation is possible. And you should contact the Office of Environmental Planning.

## Slide 37: Other Things to Consider
The Migratory Bird Treaty Act of 1918
https://www.fws.gov/program/migratory-birds
Candidate and Proposed Species
Notes: The Migratory Bird Treaty Act protects all nesting and migratory birds. This means: if you see a nest, please pause your project until you’ve contacted the Office of Environmental Planning and/or Federal-POC. Keeping in mind some nests, like hummingbird nests, are incredibly small, and others are not your typical nests like burrowing owls. It’s also recommended to do your best to avoid projects during known migratory seasons.
There are permits for intentionally moving or destroying nests/birds.
There are no permits for incidentally effecting birds (solar).
And finally, Candidate and Proposed Species, which are species for which we have enough information that we are considering them for placement on the ESA but haven’t completed the listing analysis yet. For here in Phoenix, this could include the Monarch Butterfly.
For projects that have a Candidate or Proposed species listed, it’s recommended:
- Do a review of your project and if effects are reasonably likely to happen. See if there are ways that effects could be minimized (monarch migration season).
Because neither Candidates and Proposed Species are officially listed yet, consultation isn’t required unless the proposed action may result in jeopardy of the species (or adverse mod of proposed critical habitat). But these steps are encouraged to help these species of concern.

## Slide 38: Monarch Proposed Listing
Proposed listing rule is available.
No critical habitat proposed in Arizona.
Proposed as threatened which would allow for 4(d) exceptions.
Public comment is open until March 12.
Visit: https://www.fws.gov/initiative/pollinators/save-monarch
Notes: For the Monarch the proposed 4(d) rule offers flexibility to encourage projects to include native milkweed and pollinator plants by providing exceptions for incidental take. So, if the species is listed that should help not only us as project implementers, but also the species.
Which on that note, please take some time to look at the proposed listing rule and provide comments on what you support and need! Public comment closes on March 12.

## Slide 39: Why to Remember the ESA
It’s another box to check, but if you miss “checking it”:
Your permit could be delayed or denied.
Your project could be delayed.
Your company could be vulnerable to lawsuits.
USFWS Law Enforcement could become involved.
For more information on Section 7 visit: https://www.fws.gov/service/esa-section-7-consultation
For more information on the ESA visit:
https://www.fws.gov/library/collections/endangered-species
Notes: We understand that you, as project implementors have a lot on your plates, and a lot of hoops to jump through, but please bear in mind that by not jumping through the ESA hoop, there could be increasingly severe consequences from delay of permits and your project, to liability and, in some cases law enforcement involvement.
We, in the Service, are not here to stop your projects. Rather, as stated in our mission statement, we are here to work with you to ensure completion of your project, while also conserving and protecting listed species.

## Slide 40
Questions?
Nichole Engelmann
(she/her)
U.S. Fish and Wildlife Service
Nichole_Engelmann@fws.gov

## Slide 41
Phoenix Approach to Environmental Compliance
Section 404 and Wildlife January 30, 2025

## Slide 42: Initial Natura/Cultural Resource Assessment (INCRA)
Archaeology
Historic Properties
Section 404/Sensitive Species
Internal City Environmental Review
  Every City construction project
  Early in design

## Slide 43: City Approach When we do Jurisdictional Delineations
Ephemeral vs Intermittent
PJD vs AJD
404 Permitting - notifying

## Slide 44: JD’s and 404 Permits Example of City’s Perspective
Lone Mountain Park
2022 PJD
2023 WOTUS Rule +
2024 PCN
  Drainage 3 re-route
Efficiency and Regulatory Certainty

## Slide 45: Jurisdictional Delineation Key Points
Document what is NOT Waters and what is Waters (photographs and mapping)
Use City’s JD and Project Area Geodatabase Template
If Approved JD is needed, call Tricia before starting

## Slide 46: Surface Water Administrative Regulation 1.55
Applies only to City of Phoenix-led projects
Covers construction projects and facility operations
City definition of Surface Water:
“A waterbody…that has a connection to another surface water downstream and is not otherwise regulated by Clean Water Act or similar state laws and regulations. This can include ephemeral surface water features.”

## Slide 47: 404 Consultant Guidance Document
City of Phoenix Process
Preliminary JDs and Dry Land Approved JDs
404 Nationwide Permits
401 Water Quality Certifications
Timelines
Resource Links

## Slide 48: Citywide Section 404 Coordinator
Single point for communications with U.S. Army Corps of Engineers (USACE)
Training program
Resource for all departments
Reviews Submittals for Quality and Consistency
Tricia Balluff, (602) 534-1775
  Tricia.Balluff@phoenix.gov

## Slide 49: Consultant’s Role
Provide a compliance schedule
- To interface with other project activities
High quality, professional submittals
Identify any additional compliance needs

## Slide 50: Philosophical Approach
Avoid
Minimize
Compensate
Conservative estimates
  Jurisdictional delineations
  Impacts calculations
Clarity
  Descriptions
  Impact calculations
Document all steps taken to avoid and/or minimize impacts.

## Slide 51: Preconstruction Notification Key Points
ENG Form 6082
Supplemental Pages
Impacts to Waters:
  Recent aerial
  JD highlighting
  Overlaid design plans

## Slide 52: 33 U.S.C. 408 Permitting Example: 3rd Street Pedestrian Bridge
Civil Works Engineering Permit (with NEPA)
May overlap with 404 permitting
Also applies to some FCDMC structures
Process for City-owned vs FCDMC-owned

## Slide 53
Updated September 2024
Razorback Sucker
Endangered
Arizona Cliffrose
Endangered
Southwestern
Willow Flycatcher
Endangered
Endangered
Yuma
Ridgway’s
Rail
Yellow-Billed
Cuckoo
Threatened
EXPN
Sonoran Pronghorn
California Least Tern
Endangered
Endangered
Desert Pupfish
Endangered
Gila Chub
Threatened & Endangered Species With Potential to Occur in Phoenix
Monarch Butterfly
Proposed Threatened
Mexican Wolf
EXPN
Cactus ferruginous
Pygmy owl
Threatened
Gila topminnow
Endangered

## Slide 54: ESA Section 10 Safe Harbor Agreements
USACE Civil Works Project Areas
  33 U.S.C. 408 Permitting
Covers:
  Western yellow-billed cuckoo
  Southwestern willow flycatcher
  Yuma Ridgway’s rail

## Slide 55: Mayor’s Monarch Pledge www.phoenix.gov/oep/monarch
Plant native Sonoran Desert milkweed and nectar plants
  Helps monarchs
  Strengthens native biodiversity
  Water conservation
Arizona Milkweed
Fairy duster
Gregg’s mistflower
Goodding verbena
Flattop buckwheat
Bee brush

## Slide 56: Migratory Bird Treaty Act
www.fws.gov/migratorybirds/
Burrowing owl, 99th Ave & Campbell
35th Ave Bridge, Cliff Swallow

## Slide 57: Migratory Bird Treaty Act Compliance
Do not harm or harass birds or their active nests
Once nests are vacant, can destroy (unless protected by another law)
Usually a timing issue
May need to survey for active nests
City USFWS Permits
  BUOW Blanket
  Project-Specific
  Applying for broader blanket relocation permit

## Slide 58: Biological Process Steps
Habitat
Assessment
Surveys,
if required
Identify
Constraints
Prepare
Report
OEP & Client
Department
Communicate
Coordinate!
and
Meets Agency &
City Standards

## Slide 59: Sensitive Species Construction Aids

## Slide 60: Arizona Native Plant Law
www.azda.gov/ESD/nativeplants.htm
Need to file Notice of Intent to Clear
with the Arizona Department of Agriculture for protected plants 60 days prior for City project

## Slide 61: Guidance Resources
www.phoenix.gov/oep/Section-404
INCRA Results
404 Consultant Guidance Manual
JD Geodatabase Template
Wildlife Flyers
Email or Phone Tricia

## Slide 62: Project Coordination and Documentation
Provide documentation
- Meeting minutes
- Phone conversations
Communicate, communicate, communicate!
Before contacting agencies, check with
- Office of Environmental Programs
- City Archaeologist
- City Historic Preservation Office

## Slide 63: How to Work for the City
Request for
Qualifications
(RFQs)
For Specific Projects
Environmental
On-Call Contracts
https://www.phoenix.gov/business/contract

## Slide 64
View Current City Solicitations
Register online -eProcurement Center
Sign up for the Newsletter!

## Slide 65: Environmental On-Call Contracts
Office of City Engineer
Natural/Cultural
RFQ expected: June 2025
Office of City Engineer
Environmental Site Assessment
RFQ expected: Jan/Feb 2025
Office of Arts & Culture
Archaeology
RFP expected: Spring 2025
Housing/Neighborhood Services Department
HUD NEPA
RFP expected: 2029
Aviation Department
Planning (NEPA)
SOQs due Jan 24, 2025
Aviation Department
Environmental
SOQs due Jan 31, 2025

## Slide 66: Related City Initiatives:
Tricia Balluff
Environmental Programs Manager
Office of Environmental Programs
602-534-1775
Tricia.Balluff@phoenix.gov
Thank you!
www.phoenix.gov/pdd/gsi
www.phoenix.gov/naturefestphx

## Slide 67: Networking Break
Return at 10:05am

## Slide 68
Natural & Cultural Resource
Regulatory Compliance Workshop
City of Phoenix
Arizona’s Surface Water Protection Program
January 30, 2025
Presented by:
Rosi Sherrill

## Slide 69
Arizona’s Surface Water Protection Program
The Protected Surface Waters List, or PSWL is made up of:
Protected Surface Waters [ARS 49-221(G)]:
  All WOTUS;
  Any perennial, intermittent, or ephemeral reaches and impoundments of the following Rivers:
    Bill Williams
    Colorado
    Gila
    Little Colorado
    Salt
    San Pedro
    Santa Cruz
    Verde
Non-WOTUS Protected Surface Waters; and
Historically Regulated as WOTUS, Confirmation Needed.

## Slide 70
Arizona’s Surface Water Protection Program

## Slide 72
Arizona’s Surface Water Protection Program

## Slide 73
Rosi Sherrill 602-771-4409 sherrill.laurie@azdeq.gov
AZPDES Hotline 602-771-1440 azpdes@azdeq.gov
Questions?
Thank you!

## Slide 74
City of Phoenix Historic Preservation

## Slide 75: Legal Requirements
National Historic Preservation Act (NHPA) - 1966
National Environmental Policy Act (NEPA) – 1970
NHPA Amendment – Certified Local Governments - 1980
Phoenix Zoning Ordinance - 1985
Notes: Why do you have to care about historic properties? Well, if you’re archaeologists you may not ;) Just kidding
At the federal level the National Historic Preservation Act was passed in 1966 following public outcry regarding the impacts of Urban Renewal and the Interstate Highway System on historic resources. The NHPA established the National Register of Historic Places, the criteria to evaluate historic –age properties for Register eligibility, State Historic Preservation Offices, and compliance! Section 106 of the NHPA, specifically, created regulatory compliance requirements for those projects deemed an undertaking (have federal funding, federal permits, carried out by a federal agency, etc.). That compliance was designed to take into account the potential impact of undertakings on historic properties.
The National Environmental Policy Act – which Tricia can speak to in far greater detail than I ever could – came shortly on the heels of the NHPA. A much broader, holistic approach to looking at the effects of undertakings on the environment, including historic properties. Meeting Section 106 of the NHPA fulfills the NEPA requirement to consider impacts to historic properties.
The lesser known1980 amendment to the NHPA created the Certified Local Government program. The program was designed to assist municipalities in protecting their historic resources. A municipality must get certified by NPS, through the local SHPO. Certification requirements include having an HP commission, a survey and inventory process and designation process, design guidelines and a design review process. For CLGs with staff that meet the Secretary of the Interior’s professional qualification standards, CLGs can also take on Section 106 compliance review tasks. This can be a positive thing in that “no effect” or “no adverse effect” projects can be reviewed in a shorter time frame that consulting with SHPO.
The City of Phoenix passed a Historic Preservation Zoning Ordinance in 1985 and became a CLG. The primary difference between locally designated properties and those on the National Register, is local designation is done through a zoning overlay.

## Slide 76: What does the COP HP Office do????
Design review for designated properties
R-O-W Reviews
Demolition review/hold designated properties
30-day demolition holds
Grants
Survey/Context/MPDF/Designation
Federal Compliance Reviews
Plans/Studies
Building Condition Assessments
Interpretation

## Slide 77
Built Environment

## Slide 78
Historic Designation Eligibility Criteria
SIGNIFICANCE
(a) Associated with the events that have made significant contribution to the broad patterns of our history; and/or
(b) Associated with the lives of persons significant in our past; and/or
(c) Embody the distinctive characteristics of a type, period or method of construction or that represent the work of a master or that possess high artistic values or that represent a significant and distinguishable entity whose components may lack individual distinction; and/or
(d) Have yielded or may be likely to yield information important in the understanding of our pre-history or history of the city of Phoenix.
AGE
Are at least 50 years old
INTEGRITY
Retain sufficient integrity of location, design, setting, materials, workmanship, feeling and association to convey their significance.
Notes: The word “Historic” means something very specific in our world. It’s not just old, as that would be “historic-age”. In order to be classified as historic – one must demonstrate that the property meets certain eligibility criteria.
As a standard measure, a property needs to be at least 50 years old to allow for another time for perspective with which to evaluate its significance. (Although some properties may be classified as exceptionally significant and determined eligible in advance of their meeting the 50-year threshold). After establishing the age of a property, one considers its historic context to establish a potential area of significance. There are four Criteria of significance noted above – which break down to association with important events, important persons, architecture or engineering, or information potential.
If a historic-age property doesn’t have significance it cannot be eligible for designation.
The other side of the eligibility coin is integrity. There are seven aspects of integrity that must be considered when evaluating a historically significant property. Depending upon the area of significance certain aspects of integrity may be more or less important.
If you have a historic-age property with historical significance without sufficient integrity, you don’t have a historic property.

## Slide 79
Assessing
Integrity
Notes: This guide, prepared by the former State Historic Preservation Officer helps to identify those aspects of integrity most important to retain dependent upon area of significance and property type. Again, this is really just as important as establishing a historic context and evaluating significance. Because if you don’t have integrity, you don’t have a historic property.

## Slide 80
Project Area vs Area of Potential Effect
Notes: Project area includes the entire area where the scope of work will be taking place.
Since Section 106 is concerned about effects to historic properties, the Area of Potential Effects should be defined based upon whether there could be direct/indirect effects to nearby historic properties.
Again – here I’m just discussing build environment resources.
This is an old project but helps to illustrate this concept. This was a road improvement project along Broadway Road between 7th Street and 67th Avenue. The area between 43rd Avenue to 67th was through the Salt River Floodplain and river bottom where sand and gravel pits were located. Because there were not above-ground resources in that section of the project area, the APE was defined as the properties adjacent to Broadway Road between 7th St and 43rd Ave.

## Slide 81
How do I know if it’s already been identified as Historic?
https://www.phoenix.gov/pdd/mycommunitymap
Notes: The City of Phoenix My Community Map is publicly accessible. The GIS map has a layer for historic properties. These are outlined in Orange and include properties listed on the Phoenix and National Registers as well as those that have been previously determined as eligible for designation.

## Slide 82
Identifying Historic Properties
Determine Scope of research efforts – define cutoff period
Records search for prior surveys
Aerial photos
Windshield Surveys
Archival sources (newspapers, building permits, city directories)
Interviews
Intensive Survey
Notes: Where to begin once you have your APE –
I’m going to be honest – it’s easier to pull information for prior archaeological surveys than for historic resource surveys. We’ve discussed My Community Map – which can help identify previously recorded properties but often times there will not have been prior surveys that cover historic-age properties.
Delightfully, with technology, we have a lot of information available from our desks. The Maricopa County Flood Control District as well as historicaerials.com provide a years of aerial photo data that can be used to check for extant historic-age resources (and also give you an idea about prior development).
Windshield surveys can also be used to more generally identify historic-age properties without doing intensive documentation.
Archival sources, like online newspaper searches, can provide information about specific property uses, as can city directories.
Sometimes there really isn’t much in the archival record on a property and interviews with owners can provide necessary information.
Depending upon the scope of work you are contracted for, an intensive level survey – with property by property inventory form and eligibility analysis may be required

## Slide 83
Developing Context
Broad History of Phoenix – with end date geared towards the end of development in your survey area
Property Specific Contexts – developed based on the property types identified through research/survey
Phoenix history doesn’t stop with this guy!
Bungalow Farmhouse, c. 1926
Pay-N-Takit Market, 1936
Independence Park, 1960-1965
Notes: A survey should include a broad historic context that does not end with the founding of Phoenix! With initial research, again particularly the amount of aerial photography that is available online today, it is pretty easy to establish periods of development. For our Broadway survey it was determined that the period of development stretched from 1911 to 1968. In that regard there should be some general history about Phoenix into the 1960s.
Drill down into the project area – what are the development factors there? Agricultural with small scale commercial – phasing into post-war residential and industrial development? The sky’s the limit!
That is to say, whenever you have a large survey area, you are bound to run across a number of different property types (in terms of historical use). Property types included along the Broadway Survey area included farm properties, commercial properties and residential subdivisions, to name a few. Sufficient context needs to be developed for each type in order to make an evaluation of significance.

## Slide 84
Alterations that don’t meet SOI standards
Change of use or features of setting
Demolition or Relocation
Lease, sale, or transfer of property
Noise, Atmospheric, Visual
Neglect
Cumulative
Assessing Effects
Notes: And that is really what assessing adverse effects is about – integrity. Adverse effects can by physical, direct changes to the property OR can be indirect, happen later in time, or be cumulative
The primary question is are the direct/indirect effects going to threaten the continued eligibility status of the property? This slide demonstrates the types of effects to consider. You’ll notice in the background image that when the FAA did plan to reroute the flight path over an area of phoenix with a concentrated number of historic districts, there was an argument that the auditory impacts were going to be an adverse effect and that sufficient community engagement and analysis had not been completed. The city sued the FAA and ultimately the flight path reverted to what it was before.
The lease, sale, or transfer of a property may be the most challenging one to follow here as it is based off of a perceived threat to a historic resource when it is no longer subject to Section 106 review and is generally automatically seen as an adverse effect.

## Slide 85
Helana Ruter (HPO) – 602-256-4155; helana.ruter@phoenix.gov
Main Office – 602-261-8699
Email: historic@phoenix.gov
https://www.phoenix.gov/pdd/historic-preservation

## Slide 86: Archaeology in the City of Phoenix
Christopher Schwartz, City Archaeologist
Natural & Cultural Resource Regulatory Compliance Workshop
Notes: Introduction – what is my role? I review all city projects, private developer projects, and outside agency projects to provide guidance for the proper treatment & regulatory compliance process for archaeological resources throughout the city. I’m also the liaison with a number of outside organizations such as AAC, AAS, Site Stewards, and the tribes. I have to hold a permit from the Arizona State Museum to be able to do anything at archaeological sites in the city – to visit them, record data, etc. The permit has serious requirements – they want you to have worked on all aspects of research on several projects – from the research design, fieldwork, analysis, and interpretive write-up. Every year, I need to apply for a new permit. We also have to hold an “AZSITE user agreement” to be able to access site mapping data and that requires specific qualifications. In this training I hope to make you aware of Phoenix’s archaeological resources, applicable laws and requirements, and the protocol that you will need to follow when you observe vandalism to archaeological sites in Phoenix.

## Slide 87: Pueblo Grande = S’edav Va’aki
As of 2023, read more here: www.phoenix.gov/newsroom/sedav-vaaki-museum/2705
S'edav pronounced suh-UH-dahf
Va'aki pronounced VAH-ah-kee
Notes: As of 2023, there is no more Pueblo Grande! Great pride of working at SVM is strong relationships with local Tribes and this was done at their request. Many other important initiatives driven by meaningful Tribal consultations.

## Slide 88: City Archaeology Office
Located at S’edav Va’aki Museum (SVM)
National Historic Landmark & listed on National Register of Historic Places
Donated to the City in 1924
SVM also has a repository, where City projects can be curated
  SVM repository operates independently from CAO at svmcollections@phoenix.gov

## Slide 89: City Archaeology Office Functions
Review proposed projects for impacts to cultural resources & provide recommendations for compliance with applicable regulations & policies.
Serve as liaison with Native American Tribes for cultural resources concerns & for compliance with ARS 41-844 and 41-865.
Support City Project Managers to comply with applicable archaeological regulations, ordinances, & policies.
Serve as liaison with CRM firms for developing scopes of work, reviewing fee estimates, & issuing notices to proceed.

## Slide 90: City Archaeology Office Functions
Manage citywide on-call archaeological services contracts.
Assist private developers with archaeological compliance associated with zoning stipulations & building permits.
Serve as steward for S’edav Va’aki Ruin & Irrigation Sites, Phoenix’s only National Historic Landmark, including overseeing the ruins stabilization by the SVM Mudslingers and providing input & guidance on infrastructure & interpretive projects.
Serve as liaison with the Arizona Site Steward Program for Phoenix.
Conduct professional quality archaeological research & prepare publications.

## Slide 91: Priorities as City Archaeologist

## Slide 92
https://www.phoenix.gov/parkssite/Documents/PKS_Pueblo_Grande_Museum/COP%20General%20HPTP_08-13-24.pdf
Continuity research theme
Sensitive language
Expanded culture histories (pre-/hist.)
Input from Tribes on methods, research themes
Expanded guidance on historic archaeology
PMAP data requirements
Requesting permissions for presenting &/or publishing results from City projects
New addendum treatment plan for everyone
Brief descriptions of big village sites & recent work

## Slide 93
https://www.phoenix.gov/parkssite/Documents/PKS_Pueblo_Grande_Museum/COP%20General%20HPTP_08-13-24.pdf
Continuity research theme
Sensitive language
Expanded culture histories (pre-/hist.)
Input from Tribes on methods, research themes
Expanded guidance on historic archaeology
PMAP data requirements
Requesting permissions for presenting &/or publishing results from City projects
New addendum treatment plan for everyone
Brief descriptions of big village sites & recent work

## Slide 94: Respectful Terminology
Arizona State Museum guidelines for respectful terminology
www.statemuseum.arizona.edu/crm/document/respectful-terminology

## Slide 98: CAO Guidelines for Archaeology
2025 revision in progress…
Updates to requirements for stripping buffer around Ancestors, esp. large village sites with deep deposits
Updates to invoicing instructions for consultants
  Ask the PMs before you ask us!
  Copy us, we can push non-responsive PMs
Updated Media Policy for Disturbance to Ancestral Human Remains
  Vetted by Tribes, also found in HPTP appendix

## Slide 99: Reminders
New HPTP & MDP replace old canal testing plan
Communicate early & often
  E.g., treatment plans: identify sampling percentages as early as possible
  If private and not doing Phase II until after Phase I, discuss with us before Phase II plan
Phone calls for important things like noncompliance, significant findings, etc.
  Don’t bury in an attachment
  If you do, put a note in the subject line and call us!

## Slide 101: Questions?
Christopher Schwartz, City Archaeologist
christopher.schwartz@phoenix.gov, 602-206-2474
Becky Hill, Contract Associate Archaeologist
rebecca.hill@phoenix.gov, 602-534-2412
City Archaeology Office
archaeology@phoenix.gov, 602-496-0901
SVM Repository
svmcollections@phoenix.gov

## Slide 102
Climate Change, Food Action, Energy Access, and You
Phoenix Climate Action Planning for a Sustainable and Equitable Desert City

## Slide 103
103
Phoenix
  Fifth largest city in the USA.
  Population over 1.6 million.
  517 square miles (1,339 square kilometers).
Temperatures
  Yearly average 75 F (24 C). WAS 78.6 IN 2024.
  Last year, record number of days over 110 F (43 C) at 79 days.
Rainfall
  7.2 inches (182 mm) per year. LAST YEAR 4.54 in

## Slide 104
RESILENT FOOD SYSTEM PROGRAMS
Programs for residents |  | 
Backyard Garden Program | Phoenix: Let’s Eat Local Campaign | Food Waste Watchers
Grant funding for education, training, and equipment to grow in backyards and community gardens. Installing gardens for up to 270 residents | A campaign celebrating the connection between Phoenix residents and the makers, growers, and advocates building stronger food systems in our local food communities. | Funding for up to 400 residents to receive food waste and composting education and training and access to a compost service for one year.

## Slide 106
Phoenix 2024 CAP Progress Report

## Slide 107: And You…

## Slide 108: Thank you for attending!
Open for networking until 12:30pm
Free Entry to S’edav Va’aki Museum with workshop badge
Give us your thoughts on the workshop
Presentations will be posted online:
Phoenix.gov/OEP/Section-404